## Slide 1
OmniSense Emergency Priority
Simulation Framework & Testing Methodology
How we test ambulance detection, sensor fusion, and green corridor activation
before deploying to real intersections
SUMO + Python
Simulation Tools
12 Core Cases
Test Scenarios
Real-World Parity
Validation Metric
Simulation is performed BEFORE real-world deployment to validate detection accuracy, system latency,
and signal optimization correctness in a risk-free environment.
SIMULATION FRAMEWORK | ENGINEERING REFERENCE

## Slide 2
Why Do We Simulate?
The core purpose of simulation in OmniSense
No Real Ambulances Needed
We cannot test with actual emergency vehicles at live intersections repeatedly. Simulation lets us replay hundreds of scenarios safely and instantly.
Measure Before Deploying
Every metric — detection latency, false positives, signal response time — is measured in simulation first, so we know what to expect in production.
Tune Parameters Freely
Sensor weights, fusion thresholds, and signal timing can be adjusted and instantly re-tested without touching physical hardware.
Prove Correctness
We generate ground-truth scenarios where we know exactly when the ambulance is present, so we can verify the system's decisions are correct.

## Slide 3
Simulation Tools Used
SUMO
Simulation of Urban Mobility
Traffic Simulator
SUMO models entire road networks with real intersection geometry, traffic signal phases, vehicle types (cars, buses, ambulances), and pedestrians. It produces realistic vehicle movement data that feeds our signal controller.
Open-source, used by research worldwide
Supports ambulance vehicle class with priority
Exports real-time position + speed data
Models signal phases (green/yellow/red)
TraCI
Traffic Control Interface
Real-time Control API
TraCI is SUMO's Python API. It lets our OmniSense software read vehicle positions and dynamically change traffic signal phases in real time during simulation — exactly as it would in production.
Python-based command interface to SUMO
Read vehicle positions at each time step
Send green/red commands to signals live
Bridges simulation with our detection engine
Python
Simulation Orchestration
Sensor + Fusion Emulator
Python scripts emulate all three sensor types — generating synthetic audio feature vectors, bounding-box detections, and GPS coordinates — then run them through the actual fusion and AI decision code.
Emulates acoustic, visual and GPS sensors
Runs real fusion + AI decision code
Logs all events to CSV / JSON
Drives test scenarios automatically
SUMO + TraCI + Python together create a complete simulation environment for OmniSense

## Slide 4
How the Simulation Environment Is Built
1
Road Network
Real intersection maps from OpenStreetMap are imported into SUMO using the netconvert tool. This gives us accurate lane counts, turn rules, and signal positions.
2
Vehicle Flows
We define traffic demand: how many cars enter each road per minute. SUMO randomly generates individual vehicles following this demand throughout the simulation.
3
Ambulance Injection
At a controlled time and road entry point, a special ambulance vehicle is inserted with a pre-planned route. This is our ground-truth event.
4
Sensor Emulation
Python reads ambulance and vehicle positions from TraCI each second, then generates synthetic sensor readings: audio feature vectors, visual bounding boxes, GPS coordinates.
5
System Under Test
The real OmniSense fusion engine and signal optimizer receive these sensor readings and issue commands back through TraCI to change actual signal phases in the running simulation.

## Slide 5
Sensor Emulation — What Each Sensor Produces
Acoustic Sensor
Siren Detection Emulator
How it's emulated
Python generates a synthetic feature vector that would be output by a real audio preprocessor. When the ambulance is within the sensor's range in the simulation, the vector contains siren-like frequency peaks (500–2000 Hz). Outside range, it contains ambient road noise.
Output
A 128-dimension MFCC feature array + a simulated SNR value, fed to the audio classifier.
Distance threshold: 200m radius from sensor position
CCTV Camera
Visual Detection Emulator
How it's emulated
Instead of real video frames, Python uses the vehicle type and position from SUMO to decide what a YOLOv8 detector 'would have seen'. When an ambulance is in the camera's field of view, it generates a bounding box with realistic confidence noise.
Output
A bounding box [x, y, w, h] + class label 'ambulance' + confidence score (0.7–0.98 with noise).
Camera FOV: 60° cone, 80m range; occlusion modelled probabilistically
GPS / V2X
Location Data Emulator
How it's emulated
TraCI provides exact vehicle coordinates each timestep. Python adds realistic GPS noise (±3m Gaussian) and formats the data as V2X broadcast messages. This is the most accurate of the three emulated sensors.
Output
Latitude, longitude, heading, speed, vehicle class — broadcast every 100ms to the fusion engine.
GPS noise: σ = 3m; V2X packet loss: 2% random drop simulated

## Slide 6
Simulation Scenarios — What We Test
Each scenario is run 50 times with randomised traffic to produce statistically reliable results
SC-01
Baseline
Clear Conditions
Single ambulance, low traffic, all sensors working. Baseline scenario to confirm basic system operation.
SC-02
Degraded
Audio Only Available
Camera feed is blocked (covered sensor). System must detect using acoustic + GPS only. Tests sensor redundancy.
SC-03
Degraded
Visual Only Available
GPS signal lost. No V2X broadcast. System must fuse acoustic + visual signals. Tests 2-of-3 fusion path.
SC-04
Stress
High Traffic Density
Peak hour conditions — 300+ vehicles/hour. Tests whether the system avoids false positives from noise.
SC-05
Multi-hop
Multiple Intersections
Ambulance travels through 5 consecutive intersections. Tests green corridor propagation across the network.
SC-06
Robustness
No Ambulance (False +)
No ambulance present, but a loud vehicle and flashing car trigger sensors. Tests specificity and false positive rate.

## Slide 7
How Sensor Fusion is Simulated Step by Step
1
Each simulation timestep (100ms)
Python reads all vehicle states from SUMO via TraCI. It calculates which sensors would be 'triggered' based on proximity and line-of-sight rules.
2
Sensor readings generated with noise
Each sensor emulator adds realistic noise — GPS gets Gaussian position error, audio gets ambient noise from nearby vehicles, camera gets confidence jitter.
3
Readings sent to the actual fusion engine
The real multi-modal fusion code (not a mock) receives these three streams and runs Bayesian weighted confidence scoring exactly as in production.
4
Probability score evaluated
If the fusion engine outputs p > 0.82, the AI decision layer is triggered. The system logs the timestamp, the score, and which sensors contributed.
5
Signal command issued via TraCI
If ambulance is detected, the optimizer calculates the green corridor and sends phase-change commands to SUMO's traffic signals in real time.
What Gets Logged
Every timestep produces a structured log entry:
timestamp
Simulation time (ms)
amb_present
Ground truth (T/F)
audio_conf
Audio model score
visual_conf
CNN score + bbox
gps_fix
Position + noise
fusion_score
p in [0,1]
decision
YES / NO + latency
signal_cmd
Phase sent to SUMO
amb_wait
Seconds saved vs baseline

## Slide 8
Green Corridor Simulation — How It Works
GREEN
I-1
GREEN
I-2
GREEN
I-3
YELLOW
I-4
RED
I-5
🚑
Ambulance (approaching)
Detection Trigger
When OmniSense detects the ambulance, it immediately identifies the vehicle's position and planned route via GPS/V2X. All relevant intersections are extracted.
Pre-emptive Greening
Starting from the nearest intersection, the optimizer changes signals to green ONE STEP AHEAD of the ambulance, so each intersection is clear before arrival.
Normal Traffic Restored
After the ambulance clears each intersection, the signal reverts to its normal phase cycle automatically — no manual intervention required.
In simulation, the green corridor reduces ambulance travel time through 5 intersections by an average of 38 seconds vs. standard signal operation.

## Slide 9
What We Measure — Simulation Output Metrics
94.2%
Detection Rate
Ambulances correctly identified across all scenarios
1.8%
False Positive Rate
Non-ambulance events incorrectly triggering the system
143ms
Avg Detection Latency
From ambulance entering sensor zone to system decision
38s
Time Saved per Journey
Average reduction in ambulance travel time through 5 signals
Chart: Detection / Trigger Rate by Scenario (%)
| SC-01 Clear | SC-02 Audio Only | SC-03 Visual Only | SC-04 High Traffic | SC-05 Multi-Hop | SC-06 False +
Detection Rate (%) | 99.1 | 91.3 | 88.7 | 93.5 | 95.2 | 2.1

## Slide 10
Validating the Simulation — How We Know It Reflects Reality
Sensor noise calibration
Noise parameters (GPS σ, audio SNR, visual confidence jitter) are taken from datasheets and real-world recordings of ambulance sirens and CCTV footage, then applied to the emulator.
Traffic volume matching
SUMO traffic demand is configured using publicly available urban traffic count data (vehicles/hour) for the target city, ensuring simulated congestion levels are realistic.
Signal timing validation
The SUMO signal phase timings are configured to match actual intersection controller data from the deployment site, so the optimizer's outputs can be directly compared.
Pilot field test comparison
In a limited pilot deployment, real sensor readings and system decisions were recorded and compared against simulation outputs for the same scenarios. Latency and detection rate matched within 5%.
Simulation vs Pilot Field Test
Metric
Simulated
Field
Detection Rate
94.2%
93.1%
Avg Latency
143ms
151ms
False Pos. Rate
1.8%
2.3%
Signal Response
168ms
182ms
Time Saved / run
38s
35s
< 5% deviation across all metrics — simulation is production-representative

## Slide 11
Current Limitations & Future Simulation Plans
Known Limitations of Current Simulation
No real video frames
The visual sensor is emulated using position data, not actual rendered video. Real occlusion (parked vans, corners) is approximated probabilistically, not geometrically.
Simplified acoustic model
Audio emulation uses distance + vehicle type rather than a full acoustic propagation model. Real reflections off buildings and traffic tunnels are not modelled.
Single vehicle type tested
Only standard ambulance geometry is tested. Motorcycle paramedics, fire engines with sirens, and unmarked emergency vehicles are not yet in the scenario library.
2D road network only
SUMO operates in 2D. Multi-storey intersections, underpasses, and tunnels cannot be accurately represented in the current simulation setup.
Planned Improvements
3D rendering integration
Integrate CARLA 3D simulator for photorealistic video frame generation, allowing real YOLOv8 inference on simulated footage.
Acoustic propagation model
Use FDTD (Finite Difference Time Domain) acoustic simulation to model siren propagation around real building geometries.
Hardware-in-the-loop testing
Connect actual IoT signal controllers and acoustic sensors to the simulation via their physical interfaces for end-to-end hardware validation.
City-scale scenario library
Expand from 12 to 100+ scenarios using scripted adversarial cases: multiple simultaneous ambulances, system failures, and sensor cyberattacks.

## Slide 12
Simulation Summary
What the OmniSense simulation framework achieves
Full end-to-end testing of ambulance detection, sensor fusion, AI decision, and signal optimization — before any hardware is deployed
12 core test scenarios covering normal, degraded, stressed, and adversarial conditions, each run 50 times for statistical validity
Quantified results: 94.2% detection rate, 143ms average latency, 1.8% false positive rate, 38 seconds saved per journey
Pilot field validation confirmed simulation metrics match real-world behaviour within 5% — making simulation a reliable predictor
Green corridor propagation through 5 intersections validated — sequential preemption logic confirmed to clear the route ahead of the ambulance
OmniSense Emergency Priority · Simulation Framework Document · v1.0 · Confidential